## Slide 1: 5G Exchange Open Coopetative Ecosystem The Concept
INFRASTRUCTURE PROVIDERS
A virtualized infrastructure orchestration system spanning multiple infrastructure providers.
It enables Enlarging Service Coverage and Enriching Service Portfolio of the involved service providers.
END USERS AROUND THE GLOBE
OTHER SERVICE PROVIDERS

## Slide 2: 5g Exchange Open Coopetative Ecosystem Enlarged Service Coverage
Partner Service Provider’s Coverage Area
Default Service Provider’s Coverage Area
The ecosystem makes it possible for end users to have the same user experience both in terms of functionality and service characteristics independent of their location or consumption worldwide.
This is achieved by automated resource sharing among infrastructure or online providers.
If the end user demands a service at a new location where the infrastructure is not owned by the default provider then the default provider may automatically lease resources from other providers to fulfill the service request at the desired location.
Default Service Provider’s Infrastructure
Partner Service Provider’s Infrastructure
Service resources
Service resources

## Slide 3: Critical Machine Type Communication 5G Radio & CORE for Latency Guarantees

## Slide 4: Cloud-enabled Factory Control For Complex & Cooperative Tasks, Scalability & Flexible Reconfiguration
Orchestration solution is needed for
integrated and automated handling of the (virtualized) compute and networking resources,
with fulfillment of latency and reliability requirements
considering multi-domain, multi-provider environment
Ultra-low Latency is critical for process operation: delay limit violation or/and delay variation causes serious service degradation/collapse
High reliability is required to avoid unnecessary service collapse in case of a failure on the communication path
  Deployment of virtualized Control functions has to fulfill the latency requirements
  Target Fault tolerance level can only be guaranteed by the proper isolation of networking and compute resources
~2-8ms cycle time is needed for the safe operation

## Slide 5: Multi-Provider Factory Automatization A Showcase for NFV Orchestration
Factory premise:
  Industry Cloud with computing and networking resources managed by the Factory owner + Orchestrator
  5G-based Local network (including radio, transport, required core entities) deployed and managed by the Regional Provider + Orchestrator
  Ultra-low latency is provided among devices/functions deployed at Factory premise
Reginal provider with orchestrated networking and compute resources
  Higher delay has to be considered towards Factory premise
International Provider
  Top orchestrator: integration of Regional Providers
Cloud-enabled Factory Automation control: e.g. PLC as VNF
  Can be deployed on Factory local or remote sites depending on latency, reliability requirements of the service
Multi-operator, Multi-domain hierarchical Orchestration
  Integrated and automated resource handling
  Latency and reliability requirements are considered
Regional provider
Factory premise
Orchestration
SDN
Latency=10ms
Latency=10ms
Latency=2ms
Latency=5ms
SDN
vCtrl
SDN
SDN
International provider
Orchestration
Orchestration
Orchestration
Industry Cloud deployment
Network is managed by the Regional Operator
vCtrl
vCtrl

## Slide 6: Demo details
Robot Balancing Control function (vCont) running on a Docker container
WiFI AP1
WiFI AP2
Eth 3
Eth 4
Eth 5
Eth 6
Eth 7
Eth 8
Eth 9
Eth 3
Eth 4
Eth 5
Eth 6
Eth 7
Eth 8
Eth 9
1
2
3
4
SDN1
SDN3
SDN2
SDN4
Factory premise
Remote domain
Mikrotik switch_2
4 Docker domains running on different blades of a TranquilPC cluster server
Represents Factory and Remote domain
SDN domains realized by Mikrotik SDN switches
Two WLAN Aps (TP-Link)
Balancing Robot (as Industry Device)
vCont
Mikrotik switch_1
Demo setup

## Slide 7: Case 1: Controller deployment with ultra low latency
Regional provider
Factory premise
Orchestration
SDN
Latency=10ms
Latency=10ms
Latency=2ms
Latency=5ms
SDN
SDN
SDN
International provider
Orchestration
Orchestration
Orchestration
Industry Cloud deployment
Network is managed by the Regional Operator
Service request
Service request: strict latency, but low reliability requirement
  Only duplicated Controller functions required
Orchestration is done by considering latency requirement
Low reliability level
  Fault tolerance to software errors (e.g. vContr failure)
  Partial tolerance to network failures (partially isolated network paths)
  Datacenter hardware error is critical
vCont_1
vCont_2
Req: ultra low latency
Req: ultra low latency
vCont_1
vCont_2
DC1
DC2
DC3
DC4

## Slide 8: Case 2: Reliable controller deployment
Regional provider
Factory premise
Orchestration
SDN
Latency=10ms
Latency=10ms
Latency=2ms
Latency=5ms
SDN
SDN
SDN
International provider
Orchestration
Orchestration
Orchestration
Industry Cloud deployment
Network is managed by the Regional Operator
Service request
vCont_1
vCont_2
Req: ultra low latency
Req: ultra low latency
Req: Anti-affinity
vCont_1
vCont_2
Service request: strict latency, moderate reliability requirement
Orchestration is done by considering latency + reliability requirement
Middle reliability level
  Fault tolerance to software and datacenter hardware errors (e.g. vContr failure)
  Partial tolerance to network failures (partially isolated network paths)

## Slide 9: Case 3: end-to-end reliability
Regional provider
Factory premise
Orchestration
SDN
Latency=10ms
Latency=10ms
Latency=2ms
Latency=5ms
SDN
SDN
SDN
International provider
Orchestration
Orchestration
Orchestration
Industry Cloud deployment
Latency=10ms
Latency=10ms
Latency=5ms
Service request
vCont_1
vCont_2
Req: ultra low latency
Req: relaxed latency
Req: End-to end reliability
vCont_1
vCont_2
Service request: end-to-end reliability, relaxed latency requirement on backup path
  Trade-off between latency and reliability
Orchestration is done by considering latency + reliability requirement
High reliability level: fault tolerance to any single failure
  Total resource isolation
Network is managed by the Regional Operator

## Slide 10: Horizon 2020/ 5G-PPP / 5G Exchange PROJECT INFORMATION
Coordinated by Ericsson
5 operators, 5 vendors, 5 Universities, 3 SMEs
  1,032 Person Months
  8 MEUR grant
October 2016 – June 2018
http://www.5gex.eu/
Contact: robert.szabo@ericsson.com
Coordinated by
Standardization activities
Notes: This experiment focuses on UC-6 Network Slicing and UC-9 GILAN / Roaming. The challenges consist of a service-related and an infrastructure-related part. For the service-related part, we want to demonstrate (a) the extension of an existing Evolved Packet Core (EPC)) in a data centre of operator A into the data centre of another mobile network operator (operator B) and the connection to the SGW of operator B. Furthermore (b), we want to show the deployment of typical GiLAN services (i.e. services typically residing in the GiLAN) such as CDN. This experiment thus needs an infrastructure-related requirement that is the creation of a cross-operator slice consisting of an end-to-end mix of compute, network and storage resources.
In the experiment, we will deploy a virtual EPC (e.g., OpenEPC) via a cloud orchestration template (e.g., OpenStack Heat) in the home (operator A) and the guest OpenStack (operator B) and spawn GiLANs. In the next step a connection between both GiLANs is established (e.g., via BGP VPN – Exp3). We will use user equipment (UE) emulated in an OpenEPC VM to connects/disconnect. Furthermore, we plan to show the synchronization of data bases (e.g., HSS – Home Subscriber Server).

## Slide 11: Resource orchestration of reliable c-MTC services Integrated and automated handling of network and compute resources by considering reliability and low-latency requirement
Credit:
J. Harmatos, D. Jocha, R. Szabó, B. Gerő (Ericsson) B. Németh, J. Czentye, B. Sonkoly (BME)